## Slide 1: PCB Design Assessment
 | Beginning (1 pts) | Developing (3 pts) | Accomplished (5 pts)
Board Size | Too Big (larger than 10X10cm) | Too Small (parts cramped) | Perfect size.
Design Rule Check (DRC) Connection Rule Check (CRC) violations | Both violations present | Either DRC or CRC violations, but not both | No Violations
Silk screen | More than 5 missing items | 5 or less missing information | Complete
Trace size | Power and Data traces are insufficient | Either Power or Data traces are insufficient | Good for Power and Data traces
Trace flow | More than 2 90 degree turns | 2 or less 90 degree turns | No 90 degree turns
Power/Ground Planes | Not used | Used but incorrectly, with islands. | Perfect and consistent use.
Pad connections | More than 5 incorrect pads | 5 or less incorrect pads | All pads connected at only N,S,E,W positions
Vias | More than 2 on pads | 2 or less on pads | No vias on pads
Parts placement | Totally random | Not random, but needs improvement. | All on 1 side and ordered nicely
Easy of access | More than 2 components covered/blocked. | 2 or less components covered/blocked | All parts easy to access
Daughter board connection | Not connected by connectors | Partially connected by connectors | Completely connected.
Notes: Power traces are usually 20-25mil, signal traces are 12th (default)