## Slide 1: D.A.R.K. Lock
By Youri Lavoie
(Dual Authentication RFID Keypad)

## Slide 2: Motivation
Necessity to conceptualize and build a project
Desire to create a practical, commonly used device
  Door security systems are widely used in professional/residential settings
Deepen knowledge of Arduino

## Slide 3: Outline
Introduction
Block Diagram
ATMega644P, Keypad
Power
PN532 RFID, TFT LCD
Buzzer, Solenoid
Layout
Milestones

## Slide 4: Introduction
Utilizes dual authentication for maximum security/versatility
  RFID tag/card = Physical authentication
  PIN = Knowledge-based authentication
Easy to use
  Audio and visual feedback is quickly provided to the user in the form of instructions, failure and success cues

## Slide 5: Block Diagram

## Slide 6: ATMega644P, Keypad
AtMega644P
  Powered by Sanguino
  Bootloader configured via JTAG
  Programed via USB to Serial converter
  16MHz Crystal
Keypad
  4x3 matrix style

## Slide 7: Power
12.0V – 2.0A from wall adapter, used by solenoid
5.0V, used by MC, buzzer, TFT LCD
3.3V, used by PN532 board
Power LED for diagnostics

## Slide 8: PN532 RFID, TFT LCD
PN532 RFID
  Reader/Writer breakout board
  Uses 3.3V
  Communicates via SPI
  Uses 4050 buffer to reduce 5.0V signals from MC to 3.3V
TFT LCD
  2.2” TFT LCD display
  Uses 5.0V, but can also use 3.3V
  Communicates via SPI
  Allows for clearer visual output to users
  Included SD Card slot support on breakout board

## Slide 9: Buzzer, Solenoid
Buzzer
  Uses PWM pin from MC to generate different audio cues
Solenoid
  Fail-secure electromagnet
  High current rushes through coil generating strong electromagnetic field, causing bolt retracting motion
  Spring re-engages bolt after current ceases to be supplied to coil

## Slide 10: Layout
Mostly surface mount (excluding headers, push button, and crystal)
Surface mount advantages
  More compact design
  Low component height allows for PCB to be contained below TFT breakout board
Surface mount disadvantages
  More difficult to solder
  Requires more research for components to replace previously planned through-hole components

## Slide 11: Layout

## Slide 12: GUI
Still WIP and very barebones
Basic serial controls
Writes up to 10 users’ details to microcontroller EEPROM
User details stored in .txt files selectable through combo box
  Line 1: Username
  Line 2: Whether or not user is active
  Line 3: PIN
  Line 4: RFID tag unique identifier (UID)
Writing anything other than the intended values will cause the lock to not work properly

## Slide 13: Milestones
Currently behind schedule
GUI still WIP

## Slide 14: Milestones (1st Semester)

## Slide 15: Milestones (2nd semester)

## Slide 16: Proposed Improvements
Revision v1.0 was riddled with minor issues, but was functional
Revision v1.2 addressed those issues
  Adapted TFT header to accommodate for compatible LCD
  Changed horizontal headers to correct pitch
  Buzzer actually connected to PWM pin
  No components on bottom copper
  Optimized component and mounting hole positioning
Striker lock solenoid would be better for real world implementation
Using components rated for outdoor use would increase viable deployment locations
Placing device in an enclosure

## Slide 17: QUESTIONS?
Thank you for listening.